## Slide 1: Combined FEA and MBD of the foot
Ahmad Shaikh
31st Dec, 2022

## Slide 2
Work done by me
  FEA
  Geometric Modelling
  OpenSim
Explanation of the Thesis

## Slide 3
Heel Strike Simulation

## Slide 4
F
Dynamic Implicit
Dynamic Explicit

## Slide 5
Creation of a parameterized foot model
Use of Primitives
Use of lofts and extrudes with parameterized sketches
Spherical cartilage between bones

## Slide 7: The general methodology used for combined mbd and fea of the foot
As per the thesis and similar papers

## Slide 8
Optical Motion Capture
GRF
EMG
(Optional)
Age
Weight
Physical Experiment
Patient Details
Rigid Bones connected by joints
+
Muscles
MBD Model
No footwear in model regardless of experiment
OpenSim
Joint Kinematics
Joint Moments
Muscle Forces
Gait Study
Barefoot- control run
Footwear- immediately after wearing
Footwear- after a few months
Barefoot- after a few months
Abaqus
Single instance of gait
Relative position of foot and ground
GRF
Muscle Forces
Static study for 4-6 instances of gait
Linear Elastic Bones
Connected by hyperelastic cartilage
And linear elastic tendons (bar element)
Encased in a hyperelastic soft tissue
FEA Model
Behaviour of footwear
Internal stresses of the foot

## Slide 9: MultiBody dynamics

## Slide 10
Optical Motion Capture
GRF
EMG
(Optional)
Age
Weight
Physical Experiment
Patient Details
Rigid Bones connected by joints
+
Muscles
MBD Model
No footwear in model regardless of experiment
OpenSim
Joint Kinematics
Joint Moments
Muscle Forces
Gait Study
Barefoot- control run
Footwear- immediately after wearing
Footwear- after a few months
Barefoot- after a few months
Abaqus
Single instance of gait
Relative position of foot and ground
GRF
Muscle Forces
Static study for 4-6 instances of gait
Linear Elastic Bones
Connected by hyperelastic cartilage
And linear elastic tendons (bar element)
Encased in a hyperelastic soft tissue
FEA Model
Behaviour of footwear
Internal stresses of the foot

## Slide 11
Physical Experiment
Optical Motion Capture
GRF
EMG
Experiment marker positions must match the MBD model
Any external systems that provide an external force must also be included in the study
For simple gait, GRF of the foot is sufficient
For gait with crutches/ walkers, GRF of the crutch/ walker is also needed
This is optional for regular gait. It improves the results of muscle actuation.
It is considered preferable for an impaired gait where regular muscle actuation is not observed.

## Slide 12
Optical Motion Capture
GRF
EMG
(Optional)
Age
Weight
Physical Experiment
Patient Details
Rigid Bones connected by joints
+
Muscles
MBD Model
No footwear in model regardless of experiment
OpenSim
Joint Kinematics
Joint Moments
Muscle Forces
Gait Study
Barefoot- control run
Footwear- immediately after wearing
Footwear- after a few months
Barefoot- after a few months
Abaqus
Single instance of gait
Relative position of foot and ground
GRF
Muscle Forces
Static study for 4-6 instances of gait
Linear Elastic Bones
Connected by hyperelastic cartilage
And linear elastic tendons (bar element)
Encased in a hyperelastic soft tissue
FEA Model
Behaviour of footwear
Internal stresses of the foot

## Slide 13
Rigid bones
Connected by Joints
Muscle actuators
Marker placement must match experiment
Degrees of freedom must be sufficient for study
Custom models can be created

## Slide 14
Optical Motion Capture
GRF
EMG
(Optional)
Age
Weight
Physical Experiment
Patient Details
Rigid Bones connected by joints
+
Muscles
MBD Model
No footwear in model regardless of experiment
OpenSim
Joint Kinematics
Joint Moments
Muscle Forces
Gait Study
Barefoot- control run
Footwear- immediately after wearing
Footwear- after a few months
Barefoot- after a few months
Abaqus
Single instance of gait
Relative position of foot and ground
GRF
Muscle Forces
Static study for 4-6 instances of gait
Linear Elastic Bones
Connected by hyperelastic cartilage
And linear elastic tendons (bar element)
Encased in a hyperelastic soft tissue
FEA Model
Behaviour of footwear
Internal stresses of the foot

## Slide 15
Scaling
Inverse Kinematics
Inverse Dynamics
Static Optimization
OpenSim
Optical Motion Capture
GRF
Age
Weight
Computer Muscles Control
EMG
(Optional)

## Slide 16
Scaling
Involves the scaling of the MBD model to the anthropometric measures of the subject
Uses distance between markers (an output of the motion capture experiment) or by manually specifying scale factors

## Slide 17
Inverse Kinematics

## Slide 18
Inverse Dynamics

## Slide 19
Static Optimization
The Static Optimization Tool uses the known motion of Inverse Dynamics of the model to solve the equations of motion for the unknown generalized forces (e.g., joint torques) subject to one of the following muscle activation-to-force conditions:
Objective:
S.T
n- no. of muscles
- activation level of muscle ‘m’ at a discrete timestep (0 to 1)
- Maximum force of muscle ‘m’
- moment arm about the joint axis
- torque at joint j
p- user defined constant (penalty?)

## Slide 20
Computer Muscles Control
At user-specified time intervals during a simulation, the CMC tool computes muscle excitation levels that will drive the generalized coordinates (e.g., joint angles) of a dynamic musculoskeletal model towards a desired kinematic trajectory. CMC does this by using a combination of proportional-derivative (PD) control and static optimization (figure below).
Before starting the CMC algorithm, initial states for the model are computed. The states comprise the generalized coordinates (joint angles), generalized speeds (joint angular velocities), plus any muscle states (e.g., muscle activation levels and fiber lengths). While the initial values of the generalized coordinates and speeds can be taken from the desired kinematics that you specify, the initial values of the muscle states are generally unknown. To compute viable starting muscle states, CMC is applied to the first 0.030 seconds of the desired movement. Because the muscle states are generally out of equilibrium and muscle forces can change dramatically during this initial time interval, the simulation results during this interval are generally not valid. Therefore, you should be sure to start CMC at least 0.030 seconds prior to the interval of interest.
Static optimization is used to distribute the load across synergistic actuators. It is called "static" optimization because the performance criterion (i.e., the cost index) is confined to quantities that can be computed at any instant in time during a simulation.

## Slide 22
Optical Motion Capture
GRF
EMG
(Optional)
Age
Weight
Physical Experiment
Patient Details
Rigid Bones connected by joints
+
Muscles
MBD Model
No footwear in model regardless of experiment
OpenSim
Joint Kinematics
Joint Moments
Muscle Forces
Gait Study
Barefoot- control run
Footwear- immediately after wearing
Footwear- after a few months
Barefoot- after a few months
Abaqus
Single instance of gait
Relative position of foot and ground
GRF
Muscle Forces
Static study for 4-6 instances of gait
Linear Elastic Bones
Connected by hyperelastic cartilage
And linear elastic tendons (bar element)
Encased in a hyperelastic soft tissue
FEA Model
Behaviour of footwear
Internal stresses of the foot

## Slide 24
Angles
Moments

## Slide 25
CS- control subject
DNS- Diabetic Neuropathic Subject

## Slide 26: Finite element analysis

## Slide 27
GRF
Muscle Forces
Static Study
Applied at a particular instance of gait
Repeated 4-6 times for different gait instances

## Slide 28
5% 25% 50% 75% 90%

## Slide 29
The exception
GRF and Ground-foot ankle applied as time varying inputs to the Talus (an internal bone)
Software?
Explicit/ Implicit?
Connection between skin and bones?
Cartilage?

## Slide 31
An Explicit FEA study

## Slide 32
Geometric Reconstruction of the Foot

## Slide 33: THANK YOU